## Slide 1
RTK Bootcode

## Slide 2: Agenda
Build Boot loader
On-Chip Recovery mode
Upgrade Boot loader
Rescue System
Dual Firmware Boot
Customize kernel boot arguments
Customize reserved memory for transcoding

## Slide 3: Build Boot loader RTD1619 SPI
U-Boot
Path: SDKRelease/Bootcode/U-Boot64
Build script: build.sh
Usage:
  ./build.sh RTD129x_spi
Output:
  Bootcode/U-Boot64/DVRBOOT_OUT/RTD129x_spi
  (1) Bootloader with burning program
    $(CHIP_VER) RTD1295_hwsetting_$(DDR)-nas-RTD1295_spi.bin
  (2) HWsetting
    hw_setting/$(CHIP_VER) RTD1295_hwsetting_BOOT$(DDR).bin

## Slide 4: Build Boot loader RTD1619 eMMc
U-Boot
Path: SDKRelease/Bootcode/U-Boot64
Build script: build.sh
Usage:
  ./build.sh RTD129x_emmc
Output:
  Bootcode/U-Boot64/DVRBOOT_OUT/RTD129x_emmc
  (1) Bootloader with burning program
    $(CHIP_VER) _hwsetting_$(DDR)-nas-$(CHIP)_spi.bin
  (2) HWsetting
    hw_setting/$(CHIP_VER) _hwsetting_BOOT$(DDR).bin

## Slide 5: Build Boot loader – RTD1619 SPI
U-Boot
Path: SDKRelease/Bootcode/U-Boot64
Build script: build.sh
Usage: ./build.sh RTD16xx_emmc
Output:
  SDKRelease/Bootcode/U-Boot64/DVRBOOT_OUT/RTD16xx_emmc/
  (1) Bootloader with burning program
    A01-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
  (2) Bootloader
    1. A01-Recovery-uda-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
    2. A01-Recovery-boot-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
  (3) HWsetting
    hw_setting/0001-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin

## Slide 6: Build Boot loader – RTD1619 eMMC
U-Boot
Path: SDKRelease/Bootcode/U-Boot64
Build script: build.sh
Usage: ./build.sh RTD16xx_emmc
Output:
  SDKRelease/Bootcode/U-Boot64/DVRBOOT_OUT/RTD16xx_emmc/
  (1) Bootloader with burning program
    A01-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
  (2) Bootloader
    1. A01-Recovery-uda-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
    2. A01-Recovery-boot-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
  (3) HWsetting
    hw_setting/0001-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin

## Slide 7
BOOT UP
On-Chip Recovery Mode
Boot loader
Ctrl+q
ESC
Upgrade Boot loader
Boot into System
TAB
USB/TFTP
Built-in Rescue system
Rescue system

## Slide 8: On-Chip Recovery mode – RTD 129x SPI
This mode is used for bootloader recovery when the bootloader inside is corrupted
Hyperterm is recommended to use
Press ctrl+q when booting up until following console appear
  d/g/r>
Press h and then transfer Hwsetting(3) by y-modem
  hw_setting/$(CHIP)_hwsetting_BOOT_$(DDR).bin
Press s, then enter
  98007058
  01500000
Press d and then transfer bootloader(2) by y-modem
  $(CHIP_VER)_hwsetting_BOOT_$(DDR)-nas-$(CHIP)_spi.bin
Press g to start recovery process

## Slide 9: On-Chip Recovery mode – RTD129x eMMC
This mode is used for bootloader recovery when the bootloader inside is corrupted
Hyperterm is recommended to use
Press ctrl+q when booting up until following console appear
  d/g/r>
Press h and then transfer Hwsetting(3) by y-modem
  hw_setting/$(CHIP)_hwsetting_BOOT_$(DDR).bin
Press s, then enter
  98007058
  01500000
Press d and then transfer bootloader(2) by y-modem
  $(CHIP_VER)_hwsetting_BOOT_$(DDR)-nas-$(CHIP)_emmc.bin
Press g to start recovery process

## Slide 10: On-Chip Recovery mode – RTD 16xx SPI
This mode is used for bootloader recovery when the bootloader inside is corrupted
Hyperterm is recommended to use
Press ctrl+q when booting up until following console appear
  d/g/r>
Press h and then transfer Hwsetting(3) by y-modem
  hw_setting/0001-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-spi.bin
Press d and then transfer bootloader(2) by y-modem
  A01-Recovery-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-spi.bin
Press g to start recovery process

## Slide 11: On-Chip Recovery mode – RTD16xx eMMC
This mode is used for bootloader recovery when the bootloader inside is corrupted
Hyperterm is recommended to use
Press ctrl+q when booting up until following console appear
  d/g/r>
Press h and then transfer Hwsetting(3) by y-modem
  hw_setting/0001-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
Press d and then transfer bootloader(2) -1 by y-modem
  A01-Recovery-uda-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
Press g to start recovery process
Press d and then transfer bootloader(2) -2 by y-modem
  A01-Recovery-boot-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
Press b1 to start recovery process
Press b2 to start recovery process

## Slide 12: Upgrade Boot loader
This is for boot loader upgrade when current boot loader is workable
Press ESC when booting up to enter U-Boot console
  Realtek>
Transfer bootloader with burning program(1) to DRAM
  By USB
    usb start
    fatload usb 0:1 0x1500000 A01-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_spi.bin or RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
    go 0x1500000
  By tftp
    tftp 0x1500000 A01-RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_spi.bin or RTD161x_hwsetting_BOOT_2DDR4_8Gb_s2666-nas-RTD16xx_emmc.bin
    go 0x1500000

## Slide 13: Rescue system
This is used to install install.img onto RTD129x/RTD1619
There are 2 ways to boot into rescue system
  1. use built-in rescue system
  2. use rescue system from USB or TFTP
1. For build-in rescue system, just press TAB when booting up, then the built-in rescue system is used
Once booting into rescue system, put install.img in USB top directory and plug into RTD129x/RTD1619, the install process will start automatically

## Slide 14: Rescue system
2. For rescue system from USB or TFTP, we should copy following 3 files to USB or TFTP directory
path: SDKRelease/OpenWRT-LEDE/target/linux/realtek/image/rtk-imagefile/workspace/rescue/
  1. spi.uImage
  2. rescue.spi.dtb
  3. rescue.root.spi.cpio.gz_pad.img
USB: press ESC into U-Boot console mode with USB attached and then press ‘gor’
TFTP: press ESC and then input following command
  tftp $kernel_loadaddr spi.uImage;tftp $fdt_loadaddr rescue.spi.dtb;tftp $rootfs_loadaddr rescue.root.spi.cpio.gz_pad.img;go k
put install.img in USB top directory and plug into RTD129x/RTD1619, the install process will start automatically

## Slide 15: TFTP configuration
TFTP is configurable in boot loader console mode
Press ESC into console mode and then edit tftp related environment variables
Realtek> env set ipaddr 192.168.0.9
Realtek> env set serverip 192.168.0.56
Realtek> env set gatewayip 192.168.0.254
Realtek> env set netmask 255.255.255.0
Realtek> env save
ping command can be used to test network
Realtek> ping 192.168.0.56

## Slide 16: Dual Firmware Boot

## Slide 17: Dual Firmware Boot
There are 2 copies of firmware table and images (kernel, dtb, rescue rootfs…etc) installed in RTD129x/RTD1619
Each firmware table has a sequence number (0-255)
Boot loader will choose the latest (bigger) firmware table to bootup
Once the latest firmware table or its content is corrupted, another firmware table will be chosen to bootup

## Slide 18: Customize kernel boot arguments
Path: arch/arm/lib/bootm.c
Function: set_custom_boot_args()
This function provides room to append programmable boot arguments.
For example, the path of boot device might be "/dev/mmcblk0p0" or "/dev/mmcblk0p1", depending on circumstances. This can be done by adding conditional statement in this function to control boot arguments.
The parameter "custom_boot_args" of this function is combined with kernelargs, and finally become part of kernel boot arguments.

## Slide 19: Customize Bootflow: AC-Recovery

## Slide 20: Customize Bootflow: AC-Recovery
Add Config
  ./Bootcode/U-Boot64/configs/rtd161x_qa_nas_rtk_defconfig
  CONFIG_CUSTOMIZE_FEATURES=y
  CONFIG_CUSTOMIZE_BOOTFLOW_1=y
  CONFIG_CUSTOMIZE_BOOTFLOW_1_PHASE_1=y
  ./Bootcode/U-Boot64/common/customized_bootflow_rtd161x.c
  #define PWR_KEY_IGPIO 2 (check you board before set)
  #define ACRECOVERY_PATH FACTORY_HEADER_FILE_NAME"ACRECOVERY"
  #define POWER_STAT_PATH FACTORY_HEADER_FILE_NAME"SHUTDOWN"
  #define WAKE_ON_LAN_PATH FACTORY_HEADER_FILE_NAME"WAKEONLAN”
  ./rtd-1619-mmnas-megingjord-2GB.dts
  rtk_iso_gpio: rtk_iso_gpio@98007100 {
  wakeup-gpio-list = <&rtk_iso_gpio 2 0 1>; /*rtk_gpio gpio# direction value*/
  /*direction: 0=input, 1=output; when direction=0=input, set value is useless */
  wakeup-gpio-enable = <1>; /*0=disable, 1=enable*/
  wakeup-gpio-activity = <0>;/*0=active low, 1=active high*/

## Slide 21: Customize Bootflow: AC-Recovery
Flag name: ACRECOVERY, SHUTDOWN, WAKEONLAN
User can set AC-recovery, Shutdown & WOL enable/disable by factory tool in user space.
  Enable: factory flag flag-name
  Disable: factory unflag flag-name
As flowchart, shutdown flag will be set to 0(disable) in every normal boot.
When WOL is enable, be noted that WOL flag of gMAC also needs to set enable before shutdown.
  echo 1 > /proc/net/eth0/r8169/wol_enable

## Slide 22: Customize reserved memory for transcoding
The following u-boot environment variables can be used to configure the reserved memory size for transcoding.
  ion_media_heap0_size
  ion_media_heap1_size
Usage
  Set a positive integer for the size of ion media heap 0 or 1 (unit: MB)
    If the value exceeds the max. allowable memory size, it will prompt error message and reset the heap size to default value when booting into kernel.
Realtek> env set ion_media_heap0_size 199 Realtek> env set ion_media_heap1_size 414
  Set the size of ion media heap 0 & 1 to zero
    Disable transcode
    Free the reserved memory for transcoding
    The board has to restart for this change to take effect.
Realtek> env set ion_media_heap0_size 0 Realtek> env set ion_media_heap1_size 0

## Slide 23: Customize reserved memory for transcoding
Usage
  If the board is configured as pure NAS function (that is, there is no reserved memory for transcoding), attempting to set ion_media_heap0_size or ion_media_heap1_size will prompt error message and abort.
Realtek> env set ion_media_heap0_size 10 Error: env ion_media_heap0_size is reserved for adjusting the memory size of ion media heap memreserve for ion media heap is not found.
  To enable the transcode function again, delete the environment variable ion_media_heap0_size & ion_media_heap1_size.

## Slide 24: Customize reserved memory for transcoding
Bootcode
ION Media Heap 0
ION Media Heap 1
0
0x00100000
0x03200000
0x0F900000
0xFFFFFFFF
0x16200000
0x2FD00000
Memory Layout
Audio Firmware
0x0FE00000