## Slide 1: Realtek NAS SDK
How to Change Boot Logo

## Slide 2: Agenda
How to enable boot logo?
Customize boot logo
How does boot logo stored in the storage device?
Notice
Free the reserved memory for boot logo

## Slide 3: How to enable boot logo?
Boot logo is only available for videoplayer configuration.
Otherwise, boot logo is disabled by default.

## Slide 4: Customize boot logo
Supported Boot logo Format
The customized boot logo image can be placed in the "feed" folder.
Specifying customized image file by setting the option "bootlogo_file".
Adjusting the "bootlogo_zone" to appropriate size to prevent from exceeding the storage size reserved for boot logo.
Format | Resolution
RGBA | 1920*1080

## Slide 5: How does boot logo stored in the storage device?
There is only one boot logo image stored in the flash device.
Therefore, the first and second firmware description entries both point to the same storage address.

## Slide 6: Free the reserved memory for boot logo
When booting the Linux kernel, there is a 9216 KiB memory area reserved for boot logo.
We can free the reserved memory by writing device attribute in sysfs directory.
Usage: echo 1 > /sys/devices/platform/rtk-fb/freelogo

## Slide 7: Notice
Disabling "burn_bootlogo" option means that the installer will not do bootlogo burn-in, but the boot logo file still exists in the install.img.
  Enabling boot logo display or not is controlled by the configurations in OpenWRT(nas_videoplayer.config).
  To truly remove boot logo file from install.img, the "bootlogo_file" option should leave blank. However, using configurations to disable boot logo display is the recommended way. Manually disabling "burn_bootlogo" might lead to unexpected result.