## Slide 1: Realtek NAS SDK
Image-Builder

## Slide 2: Image-Builder
Build Realtek SoC Image file
Prepare Files for Rescue System
Customization
  Specify Firmware Layout in Storage
    Edit feed.conf to descript storage layout
  Support Customer’s Root Filesystem
    Edit feed.conf to descript content of root partition
  Easy to Set
    Kernel Boot Argument
    MAC Address
    IP information for Bootcode
    Edit file, bootargs.conf.{spi,emmc,nand}

## Slide 3: install.img
Realtek SoC Image file which contains
  Bluecore.audio
  Kernel Image
  DTB for Normal Boot up
  DTB for Rescue Boot up
  Root Filesystem for Rescue System
  Root Filesystem for Normal Boot up (if eMMc or NAND)
  Layout description file, config.txt
  Storage Writer, installer

## Slide 4: Directories
build_image.sh
  Build Script
arm_bin/
  arm binary files for running in rescue system
x86_bin/
  X86 binary files for creating install.img

## Slide 5: Directories
rescue-rootfs/
  Rescue Root File System.
  Use initramfs.sh to compress/decompress rescue root filesystem image.
  Size limit is 1 MB (1048576 bytes)
    If exceeding the limit, change CONFIG_ROOTFS_RESCUE_SIZE in Bootcode's U-Boot64/include/configs/rtd161x_qa_{board}.h as in device tree
    For example, define CONFIG_ROOTFS_RESCUE_SIZE as 0x200000 in rtd161x_qa_spi_64.h when device tree has initrd-start=<0x02200000> and initrd-end=<0x02400000> where initrd start and end are defined in kernel source's include/soc/realtek/memory.h as ROOTFS_RESCUE_START and ROOTFS_RESCUE_END respectively
feed/
  Gather Firmware Files
  Edit feed.conf to descript storage layout
    Three example files, feeds.conf.emmc, feeds.conf.spi, feeds.conf.nand

## Slide 6: feed.conf Content
storage
  Define storage type
storage_size
  Define size of storage in unit of bytes
storage_align
  Define the alignment of storage block in unit of bytes
storage_eraseblock_size (NAND only)
  Define the size of erase block in unit of bytes
storage_start_address
  The start address of available are for storing firmware. DO NOT CHANGE!
lzma
  Use LZMA to compress bluecore.audio and kernel. Recommend for SPI

## Slide 7: feed.conf Content
bootargs
  Insert U-Boot variables
  Configuration File
    bootargs.conf.emmc, bootargs.conf.spi, bootargs.conf.nand
Content of bootargs.conf.{emmc,spi,nand}
  ethaddr=00:10:20:30:40:50
  gatewayip=192.168.100.254
  ipaddr=192.168.100.1
  netmask=255.255.255.0
  SPI Kernel Arguments
    kernelargs=mtdparts=RtkSFC:1024k(U-Boot)ro,64k(FWtbl)ro,128k(Factory),10944k(FW)ro,4096k(Free),128k(oops) init=/etc/init root=/dev/sda1 rootfstype=ext4 rootwait loglevel=8
  eMMc Kernel Arguments
    kernelargs=init=/etc/init root=/dev/mmcblk0p1 rootfstype=squashfs rootwait loglevel=8
  NAND Kernel Arguments
    kernelargs=init=/etc/init overlay=/dev/ubi1_0 overlayfs=ubifs rootwait loglevel=8
    For NAND, build_image.sh script will generate necessary arguments (i.e., mtdparts=, ubi.mtd=, root=, and rootfstype=) according to feeds.conf, and append them to kernelargs

## Slide 8: feed.conf Content/bootargs
Content of bootargs.conf.{emmc,spi,nand}
  ethaddr
    Device MAC address
  gatewayip Bootcode ifconfig
  ipaddr Bootcode ifconfig
  netmask Bootcode ifconfig
  Kernelargs
    Part of kernel boot arguments
    Kernel boot arguments is combined with kernelargs and bootargs in DTB files
      Bootargs = bootargs in dtb + kernelargs
      Kernelargs could be edited in bootcode and easy to change
        Init=/et/init or /lib/systemd
        root=/mmcblk0px
        rootfstype=squashfs or ext4
        loglevel

## Slide 9: feed.conf Content
update_1stfw, update_2ndfw
  Image-Builder Supports Dual Firmware Updating.
  Set to ‘y’ to update the set of firmwares.
  Set to ‘n’ to ignore the set of firmwares while burning the storage.
seqnum_1stfw, seqnum_2ndfw
  Firmware version
  Bootcode compares sequnum to decide the latest firmware set. Bigger number is the latest firmware.

## Slide 10: feed.conf Content
kerneldtb_file
  Filename of DTB for normal booting
kerneldtb_zone
  The size of a storage area for storing the kerneldtb_file
kerneldtb_1stfw_addr, kerneldtb_2ndfw_addr
  The start add of first/second kerneldtb_zone
ALL values MUST aligned by storage_align, in unit of bytes.

## Slide 11: feed.conf Content
rescuedtb_file
  Filename of DTB for rescue system booting
rescuedtb_zone
  The size of a storage area for storing the rescuedtb_file
rescuedtb_1stfw_addr, rescuedtb_2ndfw_addr
  The start add of first/second rescuedtb_zone
ALL values MUST aligned by storage_align, in unit of bytes.

## Slide 12: feed.conf Content
rescuefs_file
  Filename of initramfs image for rescue system booting
  The example file is rescue-rootfs/rescue_rootfs.cpio.gz
rescuefs_zone
  The size of a storage area for storing the rescuedtb_file
rescuefs_1stfw_addr, rescuefs_2ndfw_addr
  The start add of first/second rescuefs_zone
ALL values MUST aligned by storage_align, in unit of bytes.

## Slide 13: feed.conf Content
bluecore_file
  Filename of bluecore.audio
  The example file is Packages/fw/bluecore.audio/bluecore.audio.zip
  Unzip it first
bluecore_zone
  The size of a storage area for storing the bluecore_file
bluecore_1stfw_addr , bluecore_2ndfw_addr
  The start add of first/second bluecore_zone
ALL values MUST aligned by storage_align, in unit of bytes.

## Slide 14: feed.conf Content
kernel_file
  Filename of kernel image
  The file is kernel/arch/arm64/boot/Image
kernel_zone
  The size of a storage area for storing the kernel_file
kernel_1stfw_addr , kernel_2ndfw_addr
  The start add of first/second kernel_zone
ALL values MUST aligned by storage_align, in unit of bytes.

## Slide 15: feed.conf Content
bootlogo_file
  Filename of boot logo image
  For videoplayback configuration only
bootlogo_zone
  The size of a storage area for storing the kernel_file
bootlogo_1stfw_addr , bootlogo_2ndfw_addr
  The start address of bootlogo_zone
  By default, there is only one bootlogo file will be placed in the storage. Therefore, addr. of bootlogo in two fw. entries are the same.
For more information about customizing bootlogo, please read the readme file for boot logo.(readme.bootlogo.pdf)
ALL values MUST aligned by storage_align, in unit of bytes.

## Slide 16: feed.conf Content
bootpart_dir
  Directory name of root filesystem
  For eMMc and NAND only
  Customer can build rootfs by themselves
bootpart_type
  For eMMc, support squashfs only; for NAND, support squashfs and ubifs
bootpart_zone
  The size of a storage area for storing the boot partition
bootpart_addr
  The start address of bootpart_zone
bootpart_name and bootpart_ini (NAND only)
  MTD partition name and configuration ini-file for ubinize, respectively
ALL values MUST aligned by storage_align, in unit of bytes.

## Slide 17: feed.conf Content (EMMC and NAND only)
normalpart_count
  Count of normal partitions which decides how many normal partitions will be created (MAX=3)
normalpartX_type (X=1 or 2 or 3)
  normal partition could be treated as swap, overlay or general purpose partition according to this value (swap, overlay, or ext4 for eMMC; ubifs for NAND)
  overlay: specify this overlay partition in kernelargs
normalpartX_file
  if normalpartX_type is ext4, this will be the filename of ext4 image which will be write on storage
normalpartX_zone
  Partition size of normalpartX
normalpartX_addr
  Starting address of normalpartX
normalpartX_name, normalpartX_dir, normalpart1_ini (NAND only)
  MTD partition name, the directory for UBIFS filesystem, and configuration ini-file for ubinize, respectively
ALL values MUST aligned by storage_align, in unit of bytes.

## Slide 18: feed.conf Content (spi only)
initramfs_file
  File name of initramfs cpio compressed image
initramfs_zone
  The size of storage area for storing initramfs_file
initramfs_addr
  The starting address of initramfs_zone
ALL values MUST aligned by storage_align, in unit of bytes.

## Slide 19: How to Use Image-Builder
Prepare Firmwares
  Kernel
    arch/arm64/boot/Image
  Rescue System DTB
    arch/arm64/boot/dts/realtek/rtd16xx/rtd-1619-nas-qa-rescue.dtb
  Normal Opernation DTB
    arch/arm64/boot/dts/realtek/rtd16xx/rtd-1619-nas-mjolnir-2GB.dtb
  Bluecore.audio
    Packages/fw/bluecore.audio/bluecore.audio.zip, unzip it
  Rescue System Root Filesystem
    Image-Builder/rescue-rootfs/rescue_rootfs.cpio.gz
  Root Filesystem
    OpenWRT-LEDE/build_dir/target-aarch64_cortex-a55_glibc/root-realtek
Copy Firmwares to Image-Builder/feed

## Slide 20: How to Use Image-Builder
Edit feed/feed.conf
  Reference files, feed.conf.{spi,emmc, nand}
In Image-Builder
  Run command./build-image.sh feed
  X86/storage_layout/ layout-checker helps to check the position of each firmware zone.

## Slide 21: How to Use Image-Builder--Output
Image-Builder/install.img
  Rescue system use install.img to upgrade firmwares
Image-Builder/workspace/rescue
  Rescue system files
    {spi,emmc,nand}.uImage
    rescue.{spi,emmc,nand}.dtb
    rescue.root.{spi,emmc,nand}.cpio.gz_pad.img

## Slide 22: How to use WebUI to build config
Open Image-Builder/StorageLayoutUI/index.html
  Choose the storage type
    Emmc
    Spi
  And corresponding settings
    Bootargs
    Storage size
    Storage align
  Supports Dual Firmware Updating
    Storage 2nd firmware address
    Update firmware
    Seqnum firmware

## Slide 23: How to use WebUI to build config
Choose six files
  Device Tree
  Rescue Device Tree
  Rescue RootFS
  Bluecore
  Kernel
  Boot Partition (only emmc)
Zone MUST aligned by storage_align
Customization Normal Part
  Emmc: 0, 1, 2, 3
  Spi: none

## Slide 24: How to use WebUI to build config
Click “OK”
  You can review the layout
click “submit”
  It can produce feed.conf.{spi, emmc}
  In /home/Downloads
  Copy feed.conf.{spi, emmc} to
  RTD16xx_SDK_Develop/Image-Builder/feed