## Slide 1
RTK Kernel for RTD1619

## Slide 2: Agenda
Wake Up from GPIO
GPIO Configuration for Power Enable

## Slide 3: Wake Up from GPIO - 1/2
Modify device tree “rtk_iso_gpio” node
Ex. rtd-16xx.dtsi
/*
* Suspend GPIO control
*
* [wakeup-gpio-list]
* <&rtk_iso_gpio 10 0 1>: <10> BT wakeup host pin; <0> input, <1> output; <0> internal pull low, <1> internal pull high;
* <&rtk_iso_gpio 26 0 1>: <26> WiFi wakeup host pin; <0> input, <1> output; <0> internal pull low, <1> internal pull high;
*
* [wakeup-gpio-enable]
* Wakeup from BT: <0> disable; <1> enable;
* Wakeup from WiFi: <0> disable; <1> enable;
*
* [wakeup-gpio-activity]
* BT pin: <0> active low; <1> active high;
* WIFI pin: <0> active low; <1> active high;
*/

## Slide 4: Wake Up from GPIO - 2/2
rtk_iso_gpio: rtk_iso_gpio@98007100 {
wakeup-gpio-list = <&rtk_iso_gpio 10 0 1>,<&rtk_iso_gpio 26 0 1>;
wakeup-gpio-enable = <1>, <1>;
wakeup-gpio-activity = <0>, <0>;
};
Check GPIO wake-up configuration through sysfs
  cat /sys/kernel/suspend/gpio_wakeup_en
  cat /sys/kernel/suspend/gpio_wakeup_act

## Slide 5: GPIO Configuration for Power Enable – 1/3
Bind GPIOs in device tree
<&gpio_controler gpio_number direction value>
gpio_controler: rtk_iso_gpio
gpio_number: Pin number; iso gpio range: 0~85 , total 86 pins
direction: 0 as input, 1 as output
value:
  input value, when direction 0
<0> pad function pull-down
<1> pad function pull-up
<2> pad function pull-disable
  output value, when direction 1
<0> pad function pull-disable, default output value LOW
<1> pad function pull-disable, default output value HIGH
<2> pad function pull-up, default output value LOW
<3> pad function pull-up, default output value HIGH
<4> pad function pull-down, default output value LOW
<5> pad function pull-down, default output value HIGH
Ex. gpios = <&rtk_iso_gpio 2 1 1>; /* iso gpio 2, output high */

## Slide 6: GPIO Configuration for Power Enable – 2/3
SATA GPIO configuration
  Modify device tree “ahci_sata” node
  Ex. rtd-1619-mmnas-megingjord-2GB.dts or rtd-1619-nas-megingjord-2GB.dts
  ahci_sata: sata@9803F000 {
  gpios = <&rtk_iso_gpio 67 1 1>,
  <&rtk_iso_gpio 62 1 1>,
  <&rtk_iso_gpio 63 1 1>,
  <&rtk_iso_gpio 64 1 1>;
  sata-port@0 {
  /delete-property/ gpios;
  };
  sata-port@1 {
  /delete-property/ gpios;
  };
  };

## Slide 7: GPIO Configuration for Power Enable – 3/3
USB GPIO configuration
  Modify device tree “rtk_usb_power_manager” node
  Ex. rtd-1619-usb.dtsi
  rtk_usb_power_manager@0 {
  compatible = "Realtek,usb-manager";
  realtek,port0-power-gpio = <&rtk_iso_gpio 57 1 3>;
  realtek,port1-power-gpio = <&rtk_iso_gpio 48 1 1>;
  realtek,port2-power-gpio = <&rtk_iso_gpio 49 1 3>;
  status = "okay";
  };