## Slide 1
FFmpeg –
RTK Hardware Transcode Tutorial

## Slide 2: Agenda
Introduction
Build FFmpeg
Transcoding command line
Issue

## Slide 3: Introduction
Realtek uses RMA (RTK Media Accelerator) as wrapper layer between FFmpeg and Openmax Integration Layer
  Decoder: libavcodec/rma_dec.c
  Encoder: libavcodec/omx.c
  Wrapper library: libRMA.so
FFmpeg
Rma Decoder
OMX Encoder
RMA Wrapper
OMX
RTK Hardware

## Slide 4: Build FFmpeg
Get FFmpeg 3.3.7 source code.
  https://ffmpeg.org/releases/ffmpeg-3.3.7.tar.xz
Patch RTK FFmpeg patch. Run
  patch –p0 < 0001-FFmpeg3.3.7-RTK-HW-ACCEL.patch
Copy RTK-NAS-Transcode-Libs to target. Run
  cp -dR RTK-NAS-Transcode-Libs/usr /usr
Configure FFmpeg. You can reference build.sh to enable RMA(RTK Media Accelerator). Run
  ./configure --enable-omx --enable-rma --enable-decoder=h264_rma --enable-decoder=mpeg4_rma --enable-decoder=hevc_rma --enable-decoder=mpeg1_rma --enable-decoder=mpeg2_rma --enable-decoder=vp8_rma --enable-decoder=vp9_rma --enable-decoder=vc1_rma --enable-decoder=wmv3_rma --enable-decoder=mjpeg_rma --enable-decoder=h263_rma --enable-decoder=avs_rma --enable-encoder=h264_omx
Build and install FFmpeg. Run
  make ; make install

## Slide 5: Transcoding Command line
ffmpeg -dec_o_width 720 -dec_o_height 480 -i ./input.mp4 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero ./output.ts
[Decoder]:
dec_o_width: scaling down width (optional, default: original width)
dec_o_height: scaling down height (optional, default: original height)
auto_resize: keeping the original width/height ratio (default: 0)
dec_o_fps: set the output fps to RMA decoder (default: 0)
turbo_mode: Speedup decode performance. Suggest enabling on 4k2k case (default: 0)
rtk_version: Show verion information about RTK patch and libs (default: 0)
search_I_frm: Start to decode from first I frame (default: 1)
search_I_err_tolerance: The percentage of error MBs that an I frame can display(only valid when search_I_frm is 1, default is 3)
[Encoder]:
i_frame_interval:H264 encode I-Frame Interval, specified in seconds (default: 0, the same with decoded frame interval)
rotation: H264 encode rotation, you can choose 0, 90, 180 or 270 (default: 0)
enc_select [1]: Select which encoder(0 or 1) that you want (default: 0)
[1] RTD1619 only

## Slide 6: Scaling Down and Aspect Ratio
RTK hardware transcode can support scaling down feature
  dec_o_width/dec_o_height in decoder side
  You can input a 4k resolution video but RTK HW can only support 1920x1080 output. So you need to set dec_o_width/dec_o_height to a value less than or equal to 1920x1080.
  E.g. Transcoding a 4k input.mp4 to h264 1080p output.ts:
RTK hardware transcode can keep the original width/height ratio
  auto_resize in decoder side
  E.g. Transcoding a 4k input.mp4 to h264 480p output.ts but keeping original aspect ratio:
  ffmpeg -dec_o_width 1920 -dec_o_height 1080 -i ./input.mp4 -c:a copy -c:v h264_omx ./output.ts
  ffmpeg -dec_o_width 852 -dec_o_height 480 –auto_resize 1 -i ./input.mp4 -c:a copy -c:v h264_omx ./output.ts

## Slide 7: Output FPS
RTK hardware transcode can set output fps to a small value
  dec_o_fps in decoder side
  E.g. Transcoding a input.mp4 at 30 fps to h264 1080p output.ts at 15 fps :
  ffmpeg -dec_o_fps 15 -i ./input.mp4 -c:a copy -c:v h264_omx ./output.ts

## Slide 8: I Frame
Decode I frame only
  turbo_mode in decoder side
  It will drop all non-referenced frames. Enable this setting may cause a non-smooth video.
  E.g. Decoding only I frames and encoding to output.ts:
Find the first I frame and start to decode
  search_I_frame in decoder side
  It will drop all non-I frames until first I frame.
  You can also set search_I_err_tolerance to set the percentage of error MBs that an I frame can decode.
  ffmpeg –turbo_mode 1 -i ./input.mp4 -c:a copy -c:v h264_omx ./output.ts
  ffmpeg –search_I_frame 1 –search_I_err_tolerance 5 -i ./input.mp4 -c:a copy -c:v h264_omx ./output.ts

## Slide 9: Encoder
Output I frame interval
  i_frame_interval in encoder side
  The setting of GOP
  E.g. Transcoding with output file that I frame appears once per second:
Output video rotation
  rotation in encoder side
  It will rotate the angle of encoded video.
  E.g. Rotate the output video to 180°
  ffmpeg -i ./input.mp4 -c:a copy -c:v h264_omx -i_frame_interval 1 ./output.ts
  ffmpeg -i ./input.mp4 -c:a copy -c:v h264_omx –rotation 180 ./output.ts

## Slide 10: Encoder Selection
There are two video encode units in RTD1619. In order to get better performance, you can select different encoder when transcoding two files at the same time.
  enc_select in encoder side (Default is 0)
    0 : Use encoder 0
    1 : Use encoder 1
  E.g. Transcode MPEGII to H264 and H265 to H264 at the same time
    Bad :
    Good:
  ffmpeg -i ./mpeg2.mpeg -c:a copy -c:v h264_omx –enc_select 0 ./output1.ts
  ffmpeg -i ./h265.mp4 -c:a copy -c:v h264_omx –enc_select 1 ./output2.ts
H265 Dec
MPEG Dec
H264 Enc 0
H264 Enc 1
H265 Dec
MPEG Dec
H264 Enc 0
H264 Enc 1

## Slide 11: Issue
Conversion failed!
  Error log: Too many packets buffered for output stream 0:1.
    Add option: "-max_muxing_queue_size 1024“
    Relative FFmpeg Discussion in https://trac.ffmpeg.org/ticket/6375