## Slide 1: Realtek NAS SDK
Realtek Pstore

## Slide 2: Introduction
Write oops and panic logs to a persistent storage before the system crashes
Need a particular MTD partition on SPI flash so that the logs can survive after a restart

## Slide 3: Configuring the pstore
To enable rtk_sfc_pstore, configure the kernel with these options
  CONFIG_MTD_RTK_SFC_PSTORE=y
  CONFIG_PSTORE=y

## Slide 4: Specifying an MTD partition
Set up an MTD partition with name “oops”
The partition can be specified through kernel’s command-line parameter mtdparts
  For example, set kernelargs variable in Image-Builder's feed/bootargs.conf.spi file
    kernelargs=mtdparts=RtkSFC:1024k(U-Boot)ro,64k(FWtbl)ro,128k(Factory)ro,10944k(FW)ro,4096k(Free),128k(oops) ...
It can also be specified via the device tree

## Slide 5: Setting the parameters
The record size for each log (default is 32 KB) must be a multiple of the erase block size and can be set through the kernel command line
For example, set record size 32 KB for erasesize 4 KB
  rtk_sfc_pstore.record_size=32768

## Slide 6: Reading the logs
The log data can be read from the pstore filesystem
  mount -t pstore pstore /sys/fs/pstore
  The format for these files is dmesg-rtksfc-N, where N is the record number
To delete a stored record from the persistent storage, simply unlink the respective pstore file
  rm /sys/fs/pstore/dmesg-rtksfc-0
Note that save all files in /sys/fs/pstore/ elsewhere after a system restart
  New oops/panic logs will overwrite the existing ones