## Slide 1: Realtek NAS SDK
RTD 129x

## Slide 2: SDKRelease/Directories
Host Environment
Bootcode
Image-Builder
Kernel-Release
OpenWRT-LEDE
Packages
Toolchain

## Slide 3: Host Environment (Ubuntu 16.04)
Ubuntu 16.04
  dpkg --add-architecture i386
  apt-get update
  apt-get install git-core build-essential libssl-dev libncurses5-dev unzip gawk zlib1g-dev subversion curl wget file python gettext libxml-parser-perl zip kmod cpio automake libarchive-zip-perl libswitch-perl bsdmainutils gperf bc device-tree-compiler libc6:i386 libncurses5:i386 libstdc++6:i386 zlib1g:i386 libarchive-zip-perl

## Slide 4: Host Environment (Docker File)
FROM ubuntu:16.04
RUN sed -i 's/archive.ubuntu/tw.archive.ubuntu/g' /etc/apt/sources.list
# Setup required packages for runner and OpenWRT compilation
RUN dpkg --add-architecture i386 \
&& apt-get update \
&& apt-get install -y locales \
git-core build-essential \
libssl-dev libncurses5-dev unzip gawk zlib1g-dev \
subversion curl wget file python gettext \
libxml-parser-perl zip kmod cpio \
libswitch-perl bsdmainutils time gperf \
libc6:i386 libncurses5:i386 libstdc++6:i386 zlib1g:i386 \
libarchive-zip-perl \
&& apt-get clean
RUN locale-gen en_US.UTF-8; mkdir -p /mnt/data
RUN git config --global user.name "$USER"
RUN git config --global user.email "$USER@realtek.com"

## Slide 5: SDKRelease/Bootcode
U-Boot64
Support Storages, SPI
Rescue System
  Update Firmwares, {Kernel, DTBs, Rescue Root Filesystem, Bluecore.audio}.
  Load Rescue System from {USB, tftp, Storage}
Dual Firmware Boot
  Two Set of Firmwares in Storage
    Use sequence number to indicate latest version
  Boot from Latest Version Firmware
On-Chip Recovery Mode
Support LOGO Display while booting
Read SDKRelease/Bootcode/Docs to get details

## Slide 6: SDKRelease/ImageBuilder
Build Realtek SoC Image file
  install.img
Customization
  Specify Firmware Layout in Storage
    By feeds.conf
  Support customer’s Root Filesystem
  Easy to Set
    Kernel Boot Argument
    MAC Address
    By Bootargs.conf
  Read SDKRelease/Image-Builder/Docs to get details

## Slide 7: SDKRelease/Kernel-Release
Kernel 4.4.18
  Same version as previous OpenWRT SDK
Available DTS
  rtd-1295-nas-giraffe-2GB.dts
  rtd-1295-mmnas-giraffe-2GB.dts
  rtd-1295-videonas-giraffe-2GB.dts
  rtd-1296-nas-saola-2GB.dts
  rtd-1296-mmnas-saola-2GB.dts
  rtd-1296-videonas-saola-2GB.dts
    nas=> Pure NAS
    mmnas => Pure NAS + Transcode
    videonas => mmnas + video playback

## Slide 8: SDKRelease/Packages
FFMpeg 3.3.7
  Trandcode Functions
FFPlayer 3.3.7
  Video Playback Functions
Paragon ufs 9.4.4
RTD129x Firmwares
  Bluecore.audio
  Bluecore.audio.CVBS
Factory Tool
  Details of factory tool are described in SDKRelease/Packages/Docs

## Slide 9: SDKRelease/OpenWRT-LEDE
OpenWRT-LEDE rootfs
OpenWRT Configs
  129x_kernel4418_nas.config- for pure NAS application
  129x_kernel4418_nas_transcode.config - for transcode NAS application
  129x_kernel4418_nas_videoplayer.config – for video playback NAS application
  Target Profile
    Giraffe eMMC – install.img stored in eMMC flash for Giraffe board
    Giraffe SPI – install.img stored in SPI NOR flash for Giraffe board
    Saola eMMC – install.img stored in eMMC flash for Saola board
    Saola SPI – install.img stored in SPI NOR flash for Saola board
How to build OpenWRT
  Use Default Configuration(configs/129x_kernel4418_nas*.config)
    Enter OpenWRT-LEDE/
    cp configs/129x_kernel4418_nas.config .config
    make oldconfig; make
  Install.img
    bin/targets/realtek/rtd129x-glibc/install.img
  Rescue files
    bin/targets/realtek/rtd129x-glibc/rescue
    Files for recovery failed firmware in storage

## Slide 10: SDKRelease/Toolchain
Use gcc-arm-8.2-2018.11 from https://developer.arm.com
Run aarch64-linux-gnu.sh to get aarch64 toolchain for building Kernel stand long
Run arm-linux-gnueabihf.sh to get 32bit toolchain for building utilities for rescue rootfs. (MUST)
  To build arm32 tools using recovery fail firmwares

## Slide 11: Appendix – boot with initramfs from OpenWRT
How to support booting initramfs based on OpenWRT rootfs?(SPI only)?
  Set CONFIG_RTK_ROOTFS_INITRD=y in OpenWRT config, and initramfs image will be inside install.img after OpenWRT is built.
How large is the reserved space for initramfs?
  0x1400000
How to check the size of generated initramfs?
  The initramfs file is generated during building OpenWRT (OpenWRT-LEDE/build_dir/target-aarch64_.../linux-realtek_.../root.initrd)

## Slide 12: Appendix – boot with initramfs from OpenWRT
How to adjust the reserved space of initramfs?
  this is defined in two place
  initramfs_zone in feed.conf (Image-Builder/feed/feeds.conf.spi)
  INITRD_SIZE in dts (e.g. Kernel-Release/kernel/arch/arm64/boot/dts/realtek/rtd129x/rtd-1295-nas-giraffe-2GB-initrd.dts)

## Slide 13: Appendix – boot with customized initramfs
How to support booting initramfs from customized rootfs (normal rootfs) ?
1. Reserve memory to place normal rootfs.
Add “/memreserve/ ROOTFS_NORMAL_START ROOTFS_NORMAL_SIZE;”
in Kernel-Release/kernel/arch/arm64/boot/dts/realtek/rtd129x/$(Available DTS
)
2. Modify Kernel-Release/kernel/include/soc/realtek/memory.h “ROOTFS_NORMAL_SIZE“ the same as booting rootfs size
/* 0x02200000 ~ 0x025fffff */
#ifdef CONFIG_RTK_VMX_ULTRA
#define ROOTFS_NORMAL_START (0x4BB00000)
#define ROOTFS_NORMAL_SIZE (0x12C00000) //300MB
#else
#define ROOTFS_NORMAL_START (0x02200000)
#define ROOTFS_NORMAL_SIZE (0x00400000) //4MB
#endif

## Slide 14: Appendix – boot with customized initramfs
3. Refer to Image-Builder/rescue-rootfs/initramfs.sh to generate normal rootfs. Please take usage of lzma in path of Image-Builder/x86_bin/lzma to compress rootfs.
4. Load normal rootfs to 0x02200000 memory offset while boot-up.
  By USB
  fatload usb 0:1 normal.root.spi.cpio.gz_pad.img 0x02200000
  By tftp
  tftp 0x02200000 normal.root.spi.cpio.gz_pad.img