## Slide 1: Realtek NAS SDK
RTD 1619

## Slide 2: SDKRelease/Directories
Host Environment
Bootcode
Image-Builder
Kernel-Release
OpenWRT-LEDE
Packages
Toolchain

## Slide 3: Host Environment (Ubuntu 16.04)
Ubuntu 16.04
  dpkg --add-architecture i386
  apt-get update
  apt-get install git-core build-essential libssl-dev libncurses5-dev unzip gawk zlib1g-dev subversion curl wget file python gettext libxml-parser-perl zip kmod cpio automake libarchive-zip-perl libswitch-perl bsdmainutils gperf bc device-tree-compiler libc6:i386 libncurses5:i386 libstdc++6:i386 zlib1g:i386 libarchive-zip-perl

## Slide 4: Host Environment (Docker File)
FROM ubuntu:16.04
RUN sed -i 's/archive.ubuntu/tw.archive.ubuntu/g' /etc/apt/sources.list
# Setup required packages for runner and OpenWRT compilation
RUN dpkg --add-architecture i386 \
&& apt-get update \
&& apt-get install -y locales \
git-core build-essential \
libssl-dev libncurses5-dev unzip gawk zlib1g-dev \
subversion curl wget file python gettext \
libxml-parser-perl zip kmod cpio \
libswitch-perl bsdmainutils time gperf \
libc6:i386 libncurses5:i386 libstdc++6:i386 zlib1g:i386 \
libarchive-zip-perl \
&& apt-get clean
RUN locale-gen en_US.UTF-8; mkdir -p /mnt/data
RUN git config --global user.name "$USER"
RUN git config --global user.email "$USER@realtek.com"

## Slide 5: SDKRelease/Bootcode
U-Boot64
Support Storages, SPI
Rescue System
  Update Firmwares, {Kernel, DTBs, Rescue Root Filesystem, Bluecore.audio}.
  Load Rescue System from {USB, tftp, Storage}
Dual Firmware Boot
  Two Set of Firmwares in Storage
    Use sequence number to indicate latest version
  Boot from Latest Version Firmware
On-Chip Recovery Mode
Support LOGO Display while Booting
Read SDKRelease/Bootcode/Docs to get details

## Slide 6: SDKRelease/ImageBuilder
Build Realtek SoC Image file
  install.img
Customization
  Specify Firmware Layout in Storage
    By feeds.conf
  Support customer’s Root Filesystem
  Easy to Set
    Kernel Boot Argument
    MAC Address
    By Bootargs.conf
  Read SDKRelease/Image-Builder/Docs to get details

## Slide 7: SDKRelease/Kernel-Release
Kernel 4.9.132
RTD16xx Driver Porting
Available Device Tree
  rtd-1619-nas-mjolnir-2GB.dts
  rtd-1619-mmnas-mjolnir-2GB.dts
  rtd-1619-videonas-mjolnir-2GB.dts
  rtd-1619-nas-megingjord-2GB.dts
  rtd-1619-mmnas-megingjord-2GB.dts
  rtd-1619-videonas-megingjord-2GB.dts
  nas=> Pure NAS
  mmnas => Pure NAS + Transcode
  videonas => mmnas + video playback

## Slide 8: SDKRelease/Packages
FFMpeg 3.2.4
Paragon ufs 9.4.4
RTD1619 Firmwares
  Bluecore.audio
Factory Tool
  Details of factory tool are described in SDKRelease/Packages/Docs

## Slide 9: SDKRelease/OpenWRT-LEDE
OpenWRT-LEDE rootfs
OpenWRT Configs
  1619_kernel44_nas.config - for pure NAS application
  1619_kernel44_nas_transcode.config - for transcode NAS application
  Target Profile
    Mjolnir eMMC – install.img stored in eMMC flash for Mjolnir board
    Mjolnir SPI – install.img stored in SPI NOR flash for Mjolnir board
    Megingjord eMMC – install.img stored in eMMC flash for Megingjord board
    Megingjord SPI – install.img stored in SPI NOR flash for Megingjord board
How to build OpenWRT
  Prepare kernel source
    Unpack kernel 4.4.162 and merge all patches into Kernel-Release/kernel
  Use Default Configuration(configs/1619_kernel44_nas.config)
    Enter OpenWRT-LEDE/
    cp configs/1619_kernel44_nas.config .config
    make oldconfig; make
  Install.img
    bin/targets/realtek/rtd16xx-glibc/install.img

## Slide 10: SDKRelease/Toolchain
Use gcc-arm-8.2-2018.11 from https://developer.arm.com
Run aarch64-linux-gnu.sh to get aarch64 toolchain for building Kernel stand long
Run arm-linux-gnueabihf.sh to get 32bit toolchain for building utilities for rescue rootfs. (MUST)

## Slide 11: Appendix – 1/2
How to support booting initramfs(normal rootfs) ?
1. Reserve memory to place normal rootfs.
Add “/memreserve/ ROOTFS_NORMAL_START ROOTFS_NORMAL_SIZE;”
in Kernel-Release/kernel/arch/arm64/boot/dts/realtek/rtd16xx/rtd-1619-mmnas-megingjord-2GB.dts or rtd-1619-nas-megingjord-2GB.dts
2. Modify Kernel-Release/kernel/include/soc/realtek/memory.h “ROOTFS_NORMAL_SIZE“ the same as booting rootfs size
/* 0x02200000 ~ 0x025fffff */
#ifdef CONFIG_RTK_VMX_ULTRA
#define ROOTFS_NORMAL_START (0x4BB00000)
#define ROOTFS_NORMAL_SIZE (0x12C00000) //300MB
#else
#define ROOTFS_NORMAL_START (0x02200000)
#define ROOTFS_NORMAL_SIZE (0x00400000) //4MB
#endif

## Slide 12: Appendix – 2/2
3. Refer to Image-Builder/rescue-rootfs/initramfs.sh to generate normal rootfs. Please take usage of lzma in path of Image-Builder/x86_bin/lzma to compress rootfs.
4. Load normal rootfs to 0x02200000 memory offset while boot-up.
  By USB
  fatload usb 0:1 normal.root.spi.cpio.gz_pad.img 0x02200000
  By tftp
  tftp 0x02200000 normal.root.spi.cpio.gz_pad.img