## Slide 1: RTD1619 NAS SDK
Test Report

## Slide 2: SATA Performance
 | HDD: WD 黑標 2T | Ext4 | No File System
Thor A01 | Write (MB/s) | 199 | 208
Thor A01 | Read (MB/s) | 202 | 202
HDD : WD 黑標 2T WD2003FZEX
Test command (for Ext4):
  Write : dd if=/dev/zero of=./testfile bs=1M count=4096 oflag=direct
  Read : echo 3 > /proc/sys/vm/drop_caches ; dd if=./testfile of=/dev/null bs=1M
Test command (for no file system):
  Write : dd if=/dev/zero of=/dev/sda1 bs=1M count=4096 oflag=direct
  Read : echo 3 > /proc/sys/vm/drop_caches;dd if=/dev/sda1 of=/dev/null bs=1M count=4096
Chart: 
| write | read
ext4 | 199 | 202
no file system | 208 | 202

## Slide 3: USB 3.0 Performance
Ext4 | Transfer request size | 1M | 2M | 4M | 8M
Thor A01 | Write (KB/s) | 232,963 | 233,876 | 234,681 | 235,232
Thor A01 | Read (KB/s) | 244,701 | 246,023 | 245,839 | 245,766
HDD :
  Samgsung SSD ( + NexStar Dual Bay HARD DRIVE DOCK, Model:NST-D400S3 )
Test command :
  iozone -I -i0 -i1 -a -s1024m -y1M -q8M -f ./test.tmp
Chart: 
| 1M | 2M | 4M | 8M
Write | 232963 | 233876 | 234681 | 235232
Read | 244701 | 246023 | 245839 | 245766

## Slide 4: Ethernet Performance
Tx | Rx | Dual
942 (Mb/s) | 942 (Mb/s) | 1862 (Mb/s)
Test command (Single test)：
  server side : iperf -s -i 1
  client side : iperf -c server_ip -i 1 -t 60
Test command (Dual test)：
  server side : iperf -s -i 1
  client side : iperf -c server_ip -i 1 -t 60 -P 2 –d
  (-d, --dualtest Do a bidirectional test simultaneously )
iperf version : 2.0.5 multi-thread version

## Slide 5: Openssl Performance
The 'numbers' are in 1000s of KB per second processed. |  |  |  |  | 
Type | 16 bytes | 64 bytes | 256 bytes | 1,024 bytes | 8,192 bytes
md5 | 14,897.19 | 43,465.24 | 97,404.84 | 140,991.83 | 162,179.75
sha1 | 25,514.52 | 88,022.57 | 251,310.68 | 466,979.84 | 623,165.44
des_cbc | 20,119.17 | 20,530.82 | 20,685.14 | 20,728.83 | 20,728.49
des_ede3 | 7,337.09 | 7,428.97 | 7,450.11 | 7,457.11 | 7,460.18
aes-128_cbc | 38,036.71 | 39,525.93 | 40,054.10 | 40,250.71 | 40,288.26
aes-192_cbc | 33,517.55 | 34,823.85 | 35,276.97 | 35,426.30 | 35,362.13
aes-256_cbc | 30,134.25 | 31,095.42 | 31,485.10 | 31,574.70 | 31,580.16
sha256 | 62,007.34 | 174,242.56 | 378,386.09 | 534,356.99 | 606,595.75
sha512 | 14,829.60 | 58,813.61 | 90,343.17 | 127,421.78 | 144,689.83
Test commad : openssl speed md5 sha1 sha256 sha512 des des-ede3 aes-128-cbc aes-192-cbc aes-256-cbc rsa2048 dsa2048 | tee /tmp/sslspeed
echo ""|"" `awk 'match($0,/r[0-9]+/) {print substr($0,RSTART,RLENGTH)}' /etc/banner` `awk -v FS="": "" -v ORS="""" '/(Processor|BogoMIPS|Hardware|machine|cpu model|system type)/ { print ""| "" $2 "" "" } END { print """" }' /proc/cpuinfo` `awk -v ORS="""" '$1 ~ /OpenSSL/ {print ""| "" $2 "" |""} $1 ~ /(md5|sha)/ {print "" "" $5 "" |""} $1 ~ /(des|aes)/ {b = b "" "" $6 "" |""} $1 ~ /(rsa|dsa)/ {print b "" "" $6 "" | "" $7 "" | "";b=""""} END { print """" }' /tmp/sslspeed | sed 's/\.\(..\)k/\10/g'`

## Slide 6: Openssl Performance (Cont.)
Chart: 
| 16 bytes | 64 bytes | 256 bytes | 1,024 bytes | 8,192 bytes
md5 | 14897.19 | 43465.24 | 97404.84 | 140991.83 | 162179.75
sha1 | 25514.52 | 88022.57 | 251310.68 | 466979.84 | 623165.44
des_cbc | 20119.17 | 20530.82 | 20685.14 | 20728.83 | 20728.49
des_ede3 | 7337.09 | 7428.97 | 7450.11 | 7457.11 | 7460.18
aes-128_cbc | 38036.71 | 39525.93 | 40054.1 | 40250.71 | 40288.26
aes-192_cbc | 33517.55 | 34823.85 | 35276.97 | 35426.3 | 35362.13
aes-256_cbc | 30134.25 | 31095.42 | 31485.1 | 31574.7 | 31580.16
sha256 | 62007.34 | 174242.56 | 378386.09 | 534356.99 | 606595.75
sha512 | 14829.6 | 58813.61 | 90343.17 | 127421.78 | 144689.83

## Slide 7: Transcode Performance
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
Test_HD_HEVC_3840x2160_30p.mkv | H265 | 無聲 | 2min 9s | 3,840*2,160 | 30 | 166.875 | 64fps, 0:58 | 101fps, 0:36 | 112fps, 0:33
Test command :
#for output 1080p
ffmpeg -y -dec_o_width 1920 -dec_o_height 1080 -i 4k/Test_HD_HEVC_3840x2160_30p.mkv -max_muxing_queue_size 1024
-c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero 4k_HEVC_1080p.ts
#for output 720p
ffmpeg -y -dec_o_width 1280 -dec_o_height 720 -i 4k/Test_HD_HEVC_3840x2160_30p.mkv -max_muxing_queue_size 1024
-c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero 4k_HEVC_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i 4k/Test_HD_HEVC_3840x2160_30p.mkv -max_muxing_queue_size 1024
-c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero 4k_HEVC_480p.ts

## Slide 8: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
GoPro.mp4 | H264 | AC3 (2ch) | 1min 15s | 3,840*2,160 | 23.976 | 2,781.67 | 37fps, 0:49 | 39fps, 0:46 | 40fps, 0:44
Test command :
#for output 1080p
ffmpeg -y -dec_o_width 1920 -dec_o_height 1080 -i 4k/GoPro.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero 4k_GoPro_1080p.ts
#for output 720p
ffmpeg -y -dec_o_width 1280 -dec_o_height 720 -i 4k/GoPro.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero 4k_GoPro_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i 4k/GoPro.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero 4k_GoPro_480p.ts

## Slide 9: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
bbb_sunflower_2160p_30fps_normal.mp4 | H264 | AAC (5.1ch) | 10min 34s | 3,840*2,160 | 30 | 1,770.43 | 33fps, 9:34 | 35fps, 8:56 | 37fps, 8:39
Test command :
#for output 1080p
ffmpeg -y -dec_o_width 1920 -dec_o_height 1080 -i 4k/bbb_sunflower_2160p_30fps_normal.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero 4k_bbb_1080.ts
#for output 720p
ffmpeg -y -dec_o_width 1280 -dec_o_height 720 -i 4k/bbb_sunflower_2160p_30fps_normal.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero 4k_bbb_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i 4k/bbb_sunflower_2160p_30fps_normal.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero 4k_bbb_480p.ts

## Slide 10: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
1080p.avi | MPEG4 | MP3 (2ch) | 3min 50s | 1,920*1,080 | 23.976 | 1,054.18 | 83fps, 1:06 | 109fps, 0:50 | 113fps, 0:48
Test command :
#for output 1080p
ffmpeg -y -i avi/1080p.avi -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero avi_1080p_1080p.ts
#for output720p
ffmpeg -y -dec_o_width 1280 -dec_o_height 720 -i avi/1080p.avi -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero avi_1080p_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i avi/1080p.avi -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero avi_1080p_480p.ts

## Slide 11: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
720p.avi | MPEG4 | MP3 (2ch) | 2min 6s | 1,280*528 | 23.976 | 524.12 |  | 224fps, 0:13 | 266fps, 0:11
Test command :
#for output 720p
ffmpeg -y -i avi/720p.avi -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero avi_720p_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i avi/720p.avi -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero avi_720p_480p.ts

## Slide 12: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
1080p.mkv | H264 | AC3 ( 5.1ch) | 5min 0s | 1,920*800 | 23.976 | 2403 | 102fps, 1:10 | 127fps, 0:56 | 149fps, 0:48
Test command :
#for output 1080p
ffmpeg -y -i mkv/1080p.mkv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mkv_1080p_1080p.ts
#for output 720p
ffmpeg -y -dec_o_width 1280 -dec_o_height 720 -i mkv/1080p.mkv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mkv_1080p_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i mkv/1080p.mkv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mkv_1080p_480p.ts

## Slide 13: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
720p.mkv | H264 | AC3 ( 5.1ch) | 5min 0s | 1,280*534 | 23.976 | 285.46 |  | 210fps, 0:34 | 264fps, 0:27
Test command :
#for output 720p
ffmpeg -y -i mkv/720p.mkv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mkv_720p_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i mkv/720p.mkv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mkv_720p_480p.ts

## Slide 14: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
TOS_1080p_24fps_hevc.mkv | H265 | AC3 ( 5.1ch) | 12min 14s | 1,920*1,080 | 24 | 180.9 | 84fps, 3:28 | 165fps, 1:46 | 328fps, 0:53
Test command :
#for output 1080p
ffmpeg -y -i mkv/TOS_1080p_24fps_hevc.mkv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero TOS_1080p_1080.ts
#for output 720p
ffmpeg -y -dec_o_width 1280 -dec_o_height 720 -i mkv/TOS_1080p_24fps_hevc.mkv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero TOS_1080p_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i mkv/TOS_1080p_24fps_hevc.mkv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero TOS_1080p_480p.ts

## Slide 15: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
1080p.mp4 | H264 | AAC (2ch) | 1min 35s | 1,920*1,080 | 29.97 | 912.65 | 80fps, 0:35 | 111fps, 0:25 | 122fps, 0:23
Test command :
#for output 1080p
ffmpeg -y -i mp4/1080p.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mp4_1080p_1080p.ts
#for output 720p
ffmpeg -y -dec_o_width 1280 -dec_o_height 720 -i mp4/1080p.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mp4_1080_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i mp4/1080p.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mp4_1080p_480p.ts

## Slide 16: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
720p.mp4 | H264 | AAC (2ch) | 3min 35s | 1,280*720 | 29.97 | 912.66 |  | 165fps, 0:39 | 223fps, 0:28
Test command :
#for output 720p
ffmpeg -y -i mp4/720p.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mp4_720p_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i mp4/720p.mp4 -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mp4_720p_480p.ts

## Slide 17: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
1080p.mpg | MPEG2 | AC3 (2ch) | 1min 7s | 1,920*1,080 | 30 | 1,925.38 | 57fps, 0:36 | 88fps, 0:23 | 101fps, 0:20
Test command :
#for output 1080p
ffmpeg -y -i mpeg/1080p.mpg -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mpeg_1080p_1080p.ts
#for output 720p
ffmpeg -y -dec_o_width 1280 -dec_o_height 720 -i mpeg/1080p.mpg -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mpeg_1080p_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i mpeg/1080p.mpg -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mpeg_1080p_480p.ts

## Slide 18: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
720p.mpg | MPEG2 | AC3 (2ch) | 1min 19s | 1,280*720 | 24 | 852.51 |  | 114fps, 0:16 | 184fps, 0:10
Test command :
#for output 720p
ffmpeg -y -i mpeg/720p.mpg -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mpeg_720p_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i mpeg/720p.mpg -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero mpeg_720p_480p.ts

## Slide 19: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
1080p.wmv | WMV9 | WMA9 (5.1ch) | 5min 0s | 1,920*1,080 | 23.976 | 1,446.4 | 78fps, 1:31 | 111fps, 1:04 | 128fps, 0:55
Test command :
#for output 1080p
ffmpeg -y -i wmv/1080p.wmv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero wmv_1080p_1080p.ts
#for output 720p
ffmpeg -y -dec_o_width 1280 -dec_o_height 720 -i wmv/1080p.wmv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero wmv_1080p_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i wmv/1080p.wmv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero wmv_1080p_480p.ts

## Slide 20: Transcode Performance (Cont.)
Test files | Coding |  | Runtime | Resolution | FPS | Bitrate (KB) | 1619 FFmpeg AV trasncode use audio copy (fps, spend time) |  | 
 | Video | Audio |  |  |  |  | 1,080p | 720p | 480p
720p.wmv | WMV9 | WMA9 (5.1ch) | 1min 59s | 1,280*720 | 23.976 | 867.125 |  | 171fps, 0:16 | 249fps, 0:11
Test command :
#for output 720p
ffmpeg -y -i wmv/720p.wmv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero wmv_720p_720p.ts
#for output 480p
ffmpeg -y -dec_o_width 720 -dec_o_height 480 -i wmv/720p.wmv -max_muxing_queue_size 1024 -c:a copy -c:v h264_omx -b:v 5500k -i_frame_interval 1 -f mpegts -copyts -start_at_zero wmv_720p_480p.ts