## Slide 1
Realtek NAS SDK
Factory Tool

## Slide 2: Agenda
Configuration
Usage
Specify correct MTD partition when using SPI board

## Slide 3: Configuration
Before compiling this tool, the cross compile toolchain directory and board type should be set properly.
  If this tool is compiled as an OpenWRT package, there is no need to configure the makefile manually.
The configuration details are described in README file. (apps/utils/factory-tool/README)

## Slide 4: Usage
1. Manipulate U-Boot Environment Variables factory (load|set|save|list) [variable] [value]
2. Set U-Boot flags factory (flag|unflag) FLAGNAME
  FLAGNAME: (ACRECOVERY|SHUTDOWN)
3. Set RTC alarm factory (set|read) [timestamp]

## Slide 5: Specify correct MTD partition when using SPI board
Commands of RTK factory tool involve read/write operations to factory data stored in flash devices.
The factory data of SPI board is stored in the start of “/dev/mtd2” by default.
If the partition or the address of factory data has been modified, the related variables in source code should be modified too.
The details of how to set the read/write position of factory tool are described in README file. (apps/utils/factory-tool/README)